## Slide 1: A Weight and Balance evaluation software for conventional and unconventional aircraft design
Supervisors: Prof. A. Bottaro Dr. Jan B. Vos
Co-supervisor: Eng. A. Jungo
Corso di Laurea Magistrale in Ingegneria Meccanica – Energia ed Aeronautica Curriculum Aeronautica, A.A 2017/2018
Master Thesis Defense
Genova, 29/03/2019
Stefano Piccini

## Slide 2
A Weight and Balance evaluation software for conventional and unconventional aircraft design
CFS (Computational Fluid and Structure) Engineering
DLR (Deutsches Zentrum für Luft-und Raumfahrt)
Project Related
Aircraft 3rd Generation MDO for Innovative Collaboration of Heterogeneous Teams of Experts
Partners
Stefano Piccini
Notes: Sviluppata presso CFS  Spin-off EPFL  DLR (Agenzia spaziale Tedesca)
coordinatore progetto AGILE
Scopo  Nuova generazione di softwares
per la progettazione concettuale
e preliminare
 Nuova generazione di velivoli

## Slide 3
Conventional and Unconventional Aircraft
Blended Wing Body
Concorde®
(www.nasa.gov/centers/dryden/research/X-48B)
(www.airliners.net)
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
(www.airbus.com)
Airbus A320-neo ®
Notes: A380 A320-neo\ ratio fuse 9.5 e ratio wings 3.4,
Concorde delta wing not conventional Mach 2
X-48B, Eduard Marmet prototype by NASA and Boeing

## Slide 4
Design Process
Virtual Product (VP): a high-fidelity mathematical/numerical representation of the physical properties and the function of the product
Multidisciplinary Design Optimization (MDO)
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: 1) TLAR: Top Level Aircraft Requirements (performance/cost/range/pass..)
2) Concettuale + Preliminare + Dettagliato
3) Preliminary+dettagli (dim sedili)
4) Detailed + componenti vere
4) MDO: + Speed, modelli matematici e numerici (VP)
 Ottimizzo su aerodinamica, aeroelasticità
Conceptual Design 90% del costo senza conoscere il prodotto.
Il vecchio sistema costoso, VP riduce costi e rischi
Fidelity = Accuratezza

## Slide 5
CEASIOMpy
(Computerised Environment for Aircraft Synthesis and Integrated Optimisation Methods)
CPACS
(Common Parametric Aircraft Configuration Scheme)
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: Software di supporto per il design preliminare e concettuale
CEASIOMpy is in python language  open source.
Usa MDO basandosi su una multi-fidelity analysis
 dell’aerodinamica e della stabilità del velivolo
MODULI Tutti Interconnessi  Geometria CPACS + Aerodynamica + WB  TODO Propulsion, Mission analysis and strutturale
 permettono l’analisi di stabilità ed aeroelastica

## Slide 6
Aircraft Masses
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: Masse Velivolo Descrizione veloce Ramp + MTOM + OEM + EM
Ricordare ZFM, ZPM!!!

## Slide 7
Weight analysis
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
D.P. Raymer [18]
Beltramo (1977) [37]
Omran Al-Shamma (2013) [38]
Notes: 1) Conventional BlackBox  fitting aircraft Database
2) Conv Processo  Inizia solo con le 4 dim fondamental  Dim sedili + propone disposizione sedili 3) Unconventional + dettagliato possibile fitting per aereo specifico
 Elevata interazione utente  Pensato per ottimizzazione
 Pass surf Density + virtual thickness and density  Specify MTOM cycle (Inizia dal Wing Loading 600kgm2)
 Motori definiti dall’utente

## Slide 8
Balance analysis
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: Processo a Masse Concentrate
Differenti masse per COG and MOI
Processo identico, ma UNC  posizionamento motori  differente valutazione geometria

## Slide 9
Range analysis
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: No a Full Mission Analysis
Aiuta a controllare l’output del modulo WB
Semplificherà la connessione con il modulo di Mssion Analysis
Leggere WF
INPUT TP/WINGLET/Vcru/TSFC

## Slide 10
B777®
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | MTOM [tons] | OEM [tons] | Fuel Max [tons] | Pax. Nb
Real [32] | 348 | 145 | 146 | 440
Estimated (Error %) | 344 (≈1) | 145 (-) | 146 (-) | 441 (<1)
 | MTOM | ZFM
COGx [m] | 27.3 | 29.1
Izz [kg] | 4.71E+07 | 4.37E+07
 | MTOM | ZFM
COGx [m] | 27.3 | 29.1
 | 4.71E+07 | 4.37E+07
Aisles: 2, Abreasts: 3+3+3, Rows: 49, Cabin Crew + Pilots: 9 + 2
Notes: Conventional Module (Sulla Tesi comparazione Conv/Unc e anche slide extra)
L=63.7m, b=64,8m , Sw=436,8m2
MOSTRO SOLO MASSE PRINCIPALI, extra slide per approfondimenti

## Slide 11
B777®
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | Range* [km] | Cabin Crew + Pilots
Real [32] | 13900 | -
Estimated (Error %) | 14400 (≈1) | 10 + 3
*Range at 95% of Fuel
Notes: Range  95% Fuel
 Max Comb \circ Max Pay
 Max Range 19000 km (Record 21000km)
Crew Updated

## Slide 12
BWB
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | MTOM [tons] | OEM [tons] | Fuel Max [tons] | Pax. Nb | Cabin Crew + Pilots
Estimated | 415 | 186 | 216 | 540 | 11 + 2
 | MTOM | ZFM
COGx [m] | 17.7 | 16.2
Izz [kg] | 7.65E+07 | 3.99E+07
 | MTOM | ZFM
COGx [m] | 17.7 | 16.2
 | 7.65E+07 | 3.99E+07
Notes: Dimensions b 56,4m, L 39,6m,
Sw 863,3m^2 & Sc 319,2m^2
Pass 800 with 2 floors
Enginesx3 a 32 m  20tons tot
Variazione COG

## Slide 13
BWB
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | Range* [km] | Cabin Crew + Pilots
Estimated | 14300 | 12 + 3
*Range at 80% of Fuel
Notes: Range Good Max Payload 80% of max fuel
How to FPM

## Slide 14
Concorde®
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | MTOM [tons] | OEM [tons] | Fuel Max [tons] | Pax. Nb | Cabin Crew +Pilots
Real [43] | 185 | 79 | 96 | 120 | 3+3
Estimated (Error %) | 184 (≈1) | 80 (≈1) | 97 (≈1) | 120 (-) | 3+3 (-)
 | MTOM | ZFM
COGx [m] | 32.5 | 36.2
Izz [kg] | 2.71E+07 | 1.92E+07
 | MTOM | ZFM
COGx [m] | 32.5 | 36.2
 | 2.71E+07 | 1.92E+07
Notes: Concorde L 61,3m, b 25,2m, Sw 414m2
 Speed 600 m/s and 2160 km/h
 Parigi/NY meno di 4 ore
Ridotta passDens poiché solo business 4 × Rolls-Royce/Snecma Olympus 593  3 tons & 170kN
COG variation IMP TRIM

## Slide 15
Concorde®
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | Range* [km]
Real [43] | 7300
Estimated (Error %) | 7400 (≈2)
*Range at 95% of Fuel
Notes: Nice Range SLOPE.
LD = 5,5, real between 12,5/3,5
 Normal aircraft 15/17

## Slide 16
Conclusions
Accurate Weight and Balance estimation for conventional and unconventional aircraft
Reliable range and fuel consumption evaluation
Flexible and designed for optimization process
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Perspectives
Larger and more detailed conventional aircraft database
Propulsion and Mission analysis
Structural, aeroelasticity and stability analysis
Notes: Read

## Slide 17
Thanks for your attention
stefano.piccini94@gmail.com
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: GG LVL UP

## Slide 18
Stefano Piccini
Bibliography
A Weight and Balance evaluation software for conventional and unconventional aircraft design
[18] Daniel P. Raymer. Aircraft Design: A Conceptual Approach, Fourth Edition. AIAA
American Institute of Aeronautics & Ast., 2006. ISBN: 978-1563478291.
[32] Boeing Commercial Airplanes. 777-200LR/-300ER/-Freighter Airplane Characteristics for Airport Planning. Tech. rep. D6-58329-2, REV. E. 2015.
[37] B.W. Kimoto-D.P. Marsh M.N. Beltramo D.L. Trapp. “Parametric study of trans-
port aircraft systems cost and weight”. In: (1977). ASIN: B0007338WC
[38] R. Ali O. Al-Shamma. “Aircraft weight estimation in interactive design process”.
In: Procs 72nd Annual International Conference on Mass Properties Engineering. 2013.
[43] Federal Aviation Administration Department of Transportation. TYPE CERTIFICATE DATA SHEET, Concorde Type 1. Tech. rep. NO. A45EU. 1979.

## Slide 19
EXTRA
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design

## Slide 20
Aircraft CPACS Geometry
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
<cpacs> <vehicles> <aircraft> <model uID=""> <name> </name> <reference> </reference> <wings> </wings> <fuselages> </fuselages> <analyses>
<massBreakdown> </massBreakdown> </analyses> </model> </aircraft> <profiles> </profiles> <engines> </engines> </vehicles> <toolspecific>
<CEASIOMpy> </CEASIOMpy>
</toolspecific> </cpacs>
(Common Parametric Aircraft
Configuration Scheme)
Notes: CPACS GEOMETRY:
utente definisce profili sezioni e li collega con segmenti e specchi
CPACSxml Uniforma il linguaggio geometria e salvataggio dati
provenienti da campi differenti.
(Necessario per un progetto OpenSource)
Right  Wing, Fuselage, Analysis, MBD, Profiles, TS CEASIOMp.

## Slide 21
Linear Regression Method
Fuselage Length
m
Wing Span based
m
Wing Area based
Self adjustable
LRM
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: 3 Groups autofitting adustable LRM

## Slide 22
OEM
Beltramo (1977) [37]
Omran Al-Shamma (2013) [38]
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Conventional module
KC = 1,04 Wing with variable sweep
0,96 < a < 1,63 = (, Aircraft Type)
c = -0,05 Turboprop, -0,08 Turbofan
Unconventional module
Structure Mass
Systems Mass
D.P. Raymer [18]
Engine Mass
Notes: t = 1.4E-04 rho = 2700 kg/m3
READ equations

## Slide 23
Unconventional OEM Parameters Influence
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
OEM vs LD
OEM vs Pax Surface Density [kg/]
OEM vs Virtual Thickness
Notes: Effect on parameters

## Slide 24
Passengers Evaluation
Conventional Seat Disposition
Unconventional Module Passenger Surface Density
[pax/]
BWB
Half Cabin
Manual Test
Nose
Tail
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: Passengers Nice
Tal about Exit Passnegers
Remeber to mention the central aisle in the BWB

## Slide 25
Flight Phases & Breguet Range
C = Specific Fuel Consumption (SFC) [1/h]
V = Aircraft cruise Speed [km/h]
L/D = Lift over Drag coefficient
W = Aircraft Weight [N]
Typical Jet SFC’s [1/hr] | Cruise
High-bypass turbofan | 0.5
Turboprop | 0.7
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: Range Braguett
Brake Horse Power and propeller efficiency

## Slide 26
Aircraft Balance – Lumped Masses
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Centre of Gravity
Moments of Inertia
Notes: Ogni nodo ha massa diversa in relazione alla sua posizione Spacing tra nodi, scelto ottimale
(TEST cilindro pieno Hp corpo rigido)
ma può essere definito dall’utente

## Slide 27
Aircraft Balance
Centre of Gravity and Moments of Inertia
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Notes: Roll, Pitch and Yaw Moments
Symmetry someone zero

## Slide 28
Aircraft inside Database: Avg. Error = 3%
Small aircraft (Fuselage Length < 40m): Max. Error < 3%
Boeing 747 and Airbus A380: Max. Error 3% and 5%
Aircraft not inside Database: Avg. Error < 6%
Passengers nb.: Error < 10% (with Default)
Exact Passengers nb. if precise seat dimensions
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Database test for conventional aircraft
Notes: Speed Read
DATI VELIVOLI REALI OTTENUTI DA:
Certificazioni FAA, ICAO, EASA
Manual for airport planning

## Slide 29
Database Test
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Manufacturer |  | Airbus | Airbus | Boeing | Boeing | Embraer | Cessna
Type |  | A321 | A380 | 737 | 747 | ERJ140 | Turboprop
Model |  | neo | 800 | 800 | 8 | LR | C208
Wing Area [] |  | 122 | 845 | 125 | 554 | 51,2 | 25,9
Wing Span [m] |  | 35,8 | 79,5 | 34,3 | 68,5 | 21,0 | 15,9
Fuselage Length [m] |  | 44,5 | 72,7 | 39,5 | 76,4 | 28,5 | 11,5
Fuselage Width [m] |  | 3,95 | 7,14 | 3,77 | 6,50 | 2,28 | 1,73
MTOM [tons] | Real | 97.0 | 575 | 7.0 | 448 | 21.1 | 3.60
 | Estimated | 95.0 | 579 | 79.3 | 426 | 21.0 | 3.60
 | Error [%] | ≈2 | <1 | <1 | ≈5 | <1 | 0
OEM [tons] | Real | 50.0 | 277.0 | 41.4 | 220 | 12.0 | 2.10
 | Estimated | 52.0 | 272.0 | 43.8 | 205 | 12.0 | 2.10
 | Error [%] | ≈4 | ≈2 | ≈6 | ≈6 | ≈0 | 0
Max. Fuel Volume [] | Real | 32.9 | 254 | 26.0 | 239 | 6.40 | 1.30
 | Estimated | 31.4 | 258 | 26.0 | 227 | 6.10 | 1.20
 | Error [%] | ≈5 | ≈2 | ≈0 | ≈5 | ≈4 | ≈2
Max. Passenger nb. | Real | 240 | 853 | 189 | 605 | 81 | 9
 | Estimated | 228 | 850 | 170 | 600 | 81 | 10
 | Error [%] | ≈5 | <1 | ≈10 | ≈1 | 0 | 10
Manufacturer |  | Airbus | Airbus | Boeing | Boeing | Embraer | Cessna
Type |  | A321 | A380 | 737 | 747 | ERJ140 | Turboprop
Model |  | neo | 800 | 800 | 8 | LR | C208
 |  | 122 | 845 | 125 | 554 | 51,2 | 25,9
Wing Span [m] |  | 35,8 | 79,5 | 34,3 | 68,5 | 21,0 | 15,9
Fuselage Length [m] |  | 44,5 | 72,7 | 39,5 | 76,4 | 28,5 | 11,5
Fuselage Width [m] |  | 3,95 | 7,14 | 3,77 | 6,50 | 2,28 | 1,73
MTOM [tons] | Real | 97.0 | 575 | 7.0 | 448 | 21.1 | 3.60
 | Estimated | 95.0 | 579 | 79.3 | 426 | 21.0 | 3.60
 | Error [%] | ≈2 | <1 | <1 | ≈5 | <1 | 0
OEM [tons] | Real | 50.0 | 277.0 | 41.4 | 220 | 12.0 | 2.10
 | Estimated | 52.0 | 272.0 | 43.8 | 205 | 12.0 | 2.10
 | Error [%] | ≈4 | ≈2 | ≈6 | ≈6 | ≈0 | 0
 | Real | 32.9 | 254 | 26.0 | 239 | 6.40 | 1.30
 | Estimated | 31.4 | 258 | 26.0 | 227 | 6.10 | 1.20
 | Error [%] | ≈5 | ≈2 | ≈0 | ≈5 | ≈4 | ≈2
Max. Passenger nb. | Real | 240 | 853 | 189 | 605 | 81 | 9
 | Estimated | 228 | 850 | 170 | 600 | 81 | 10
 | Error [%] | ≈5 | <1 | ≈10 | ≈1 | 0 | 10
Notes: Error lower than 6 percent for masses
Error higher for passengers because of the defualt value for seast
Can be adjusted easly
Remeber Exit Passengers

## Slide 30
Balance Test
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Stefano Piccini
Notes: Front - 15m
Back + 10m

## Slide 31
Balance Test
A Weight and Balance evaluation software for conventional and unconventional aircraft design
Stefano Piccini
Mass [tons] | 
MTOM | 269
OEM | 124
FUEL | 96
Max Payload (MTOM) |  | MOI [kg] |  |  |  | 
Wing Placement (x, y, z) [m] | COG (x, y, z) [m] |  |  |  |  | 
L) (9.5, 0.0, 4.4) | (27.3, 0.0, 5.3) | 1.12E+07 | 6.04E+07 | 7.07E+07 | 0 | 2.20E+06
C) (24.5, 0.0, 4.4) | (32,5, 0.0, 5.3) | 1.12E+07 | 4.51E+07 | 5.51E+07 | 0 | 1.03E+06
R) (34.5, 0.0, 4.4) | (36, 0.0, 5.3) | 1.12E+07 | 5.00E+07 | 6.00E+07 | 0 | 2.56E+05
Max Payload (MTOM) |  |  |  |  |  | 
Wing Placement (x, y, z) [m] | COG (x, y, z) [m] |  |  |  |  | 
L) (9.5, 0.0, 4.4) | (27.3, 0.0, 5.3) | 1.12E+07 | 6.04E+07 | 7.07E+07 | 0 | 2.20E+06
C) (24.5, 0.0, 4.4) | (32,5, 0.0, 5.3) | 1.12E+07 | 4.51E+07 | 5.51E+07 | 0 | 1.03E+06
R) (34.5, 0.0, 4.4) | (36, 0.0, 5.3) | 1.12E+07 | 5.00E+07 | 6.00E+07 | 0 | 2.56E+05
L
C
R
Notes: COG varia
Inerzia CRESCE  distanza relativa dal COG CRESCE
Ixz DECRESCE COG davanti ala Combustibile maggior elemento di influenza
Test No combustibile COG quasi costante

## Slide 32
Box-Wing
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | MTOM [tons] | OEM [tons] | ZFM [tons] | Pax. Nb | Cabin Crew+ Pilots | Range* [1000 km]
Estimated | 62 | 32 | 51 | 180 | 4+2 | 5.3
 | MTOM
COGx [m] | 17.2
Izz [kg] | 4.35E+06
 | MTOM
COGx [m] | 17.2
 | 4.35E+06

## Slide 33
ATR72®
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design
 | MTOM [tons] | OEM [tons] | ZFM [tons] | Pax. Nb | Cabin Crew+ Pilots | Range* [1000 km]
Real | 23 | 13 | 21 | 70 | 2+2 | 1.5
Estimated (Error %) | 23 (-) | 13 (-) | 21 (-) | 72 (≈+2) | 2+2 (-) | 1.4 (-3,27)
 | MTOM
COGx [m] | 12.3
Izz [kg] | 9.94E+05
 | MTOM
COGx [m] | 12.3
 | 9.94E+05
*Range at 50% of Fuel
Aisles: 1, Abreasts: 1+2, Rows: 24

## Slide 34
B777® Parameters Example
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design

## Slide 35
B777® Masses Comparison
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design

## Slide 36
B777® Ranges and Inertia Comparison
Stefano Piccini
A Weight and Balance evaluation software for conventional and unconventional aircraft design