## Slide 1: Investigation of thermoacoustic instabilities in a simple model of a gas turbine combustor
Supervisor: Students:
Prof. Alessandro Bottaro Lorenzo Carrattieri
Giulia Innocenti

## Slide 2: What is thermoacoustic instability?
Necessity to reduce NOx emissions
New combustion techniques:
LP combustion
Thermoacoustic Instability
Thermoacoustic instability is an unsteady phenomenon and occurs at well-defined frequencies.
A loud sound develops in the combustion chamber (humming).

## Slide 3: Unsteady combustion generates acoustic waves, which alter the inlet flow rates of fuel and air. At lean premixed conditions, this leads to a significant unsteady heat release rate. If the phase relationship is suitable, self-excited oscillations will grow in a confined space.
Unsteady combustion
Acoustics
This is the basic idea of positive feedback.

## Slide 4: Structure of the thesis
This work aims to investigate the thermoacoustic behavior of the premixed combustor model described by Dowling and Stow [1].
Linear
Nonlinear
TALOM*
Ansys Fluent
Approach
*(Thermo-Acoustic Low-Order Modelling)
[1] Acoustic Analysis of Gas Turbine Combustors, Journal of propulsion and power, 19(5):751–764, 2003.

## Slide 5: The Rayleigh criterion
Acoustic driving
Acoustic damping
Crocco’s flame model [2] :
If the acoustic driving is greater than the damping effect over a time interval, then thermoacoustic instabilities will set in: self-excited oscillations.
TALOM approach
[2] T. C. Lieuwen. Unsteady combustor physics. Cambridge University Press, 2012.

## Slide 6: The TALOM approach, linear analysis
The evolving flow is considered to be one-dimensional, inviscid, and mean flow parameters uniform in each of the three ducts.
The inlet is choked (ṁin=0.05 kg/s, Tin= 300 K).
The outlet is defined as a pressure outlet (patm = 1.01 x 105 Pa).
Compact flame with a temperature of 2000 K.

## Slide 7: Linear analysis: results
The perturbed system is solved as an eigenvalue problem in the complex domain (asymptotic behavior).
Whose real part corresponds to the frequency of the oscillation and the negative imaginary part represents the growth rate.
For k=0 no unsteady heat release rate is provided.

## Slide 8: Linear analysis: results
For k=1 an unsteady heat release rate is provided.
The time lag τ (fuel convection time from injection to its combustion) is set equal to 6 milliseconds.
The mass flow rate fluctuation is sampled in the premixer.

## Slide 9: Variation of the time lag τ
We see a strong variability of the resulting modes, which are greatly dependent on the time lag τ.

## Slide 10: Variation of the flame model
Mode trajectories are similar to the previous case. Again, there is a strong variability of the resulting modes.
New flame model:

## Slide 11: Ansys, nonlinear analysis
No combustion model was implemented. Control of the source term of the flame energy eq.
Given the dimensions of the control volume, its thickness has been set equal to 2.5 millimeters, so that it can be considered adequately thin.
Flame

## Slide 12: Mesh

## Slide 13: Setup of the simulation
15 cases in total
Evolving fluid: air
2D axisymmetric simulation (RANS-URANS)
Turbulence model: k-ω SST
Energy equation: active
Mass flow rate inlet: 0.05 kg/s (300 K)
Pressure outlet: 1.01 x 105 Pa
Adiabatic walls
Control of the energy source term for the flame zone:
Q
Q’
d = 5, 17, 20 mm from the flame location (premixer)
β = 1, 1.5, 1.6, 1.7, 2

## Slide 14: Unsteady heat addition
Stable cases | Unstable cases
d=5 mm, β=1, 1.5, 1.6 | d=5 mm, β=1.7, 2
d=17 mm, β=1, 1.5 | d=17 mm, β=1.6, 1.7, 2
d=20 mm, β=1, 1.5 | d=20 mm, β=1.6, 1.7, 2
Limit cycle
Decay

## Slide 15: Example of a limit cycle state
Static temperature [K]
Axial velocity [m/s]
d=20 mm, β=2

## Slide 16: Acoustic energy
Limit cycle amplitude
Exponential growth

## Slide 17: Acoustic energy growth rates

## Slide 18: Acoustic energy limit cycles

## Slide 19: Acoustic energy limit cycles

## Slide 20: How to reduce thermoacoustic instabilities?
Thermoacoustic instability occurs in the feedback between combustor acoustics fluctuations and the heat release fluctuations through a coupling mechanism.
This coupling must be broken to control or even eliminate thermoacoustic instabilities.
Unsteady heat release fluctuations Q ̍
Acoustic fluctuations p ̍, u ̍

## Slide 21: How to reduce thermoacoustic instabilities?
The aim is to design an actuator, such as a loudspeaker, to produce antisound in order to damp the thermoacoustic instabilities.
COMBUSTOR DAMPING (resistive devices)
ACOUSTIC ENERGY (reactive devices)
Active control
Passive control
The thermoacoustic instabilities can be controlled through two main techniques:

## Slide 22: How to reduce thermoacoustic instabilities?
Porous medium
Helmholtz resonators
In this study, passive control has been implemented through the following damper devices:
resistive devices  porous membranes  porous medium
reactive devices  acoustic cavities  Helmholtz resonator

## Slide 23: Porous media
Porous media are solid and heterogeneous materials having voids, called pores, in their microstructure and they can be traversed by the fluids.
Porosity [-]
·
2 cases in total
Porous medium before the flame
Porous medium after the flame

## Slide 24: Porous medium before the flame
POROUS ZONE
Porosity ε = 0.75
Pore sphericity
Pore diameter Dp = 0.8 mm
Permeability k = 2.88 · 10−08 m2
Inertial coefficient C2 = 2593 m-1
Thermal model: equilibrium
Setup of the simulation
Geometry

## Slide 25: Porous medium before the flame: results
Porosity [-] | ∆P [kPa] | Mean axial velocity [m/s] | 
0.75 | 24 | 23.7 | 25-30
0.85 | 10 | 26.4 | 15-20
0.9 | 6 | 27.5 | 5-10
Porosity [-] | ∆P [kPa] | Mean axial velocity [m/s] | 
0.75 | 24 | 23.7 | 25-30
0.85 | 10 | 26.4 | 15-20
0.9 | 6 | 27.5 | 5-10
The next table shows the results by varying porosity.
ε

## Slide 26: Porous medium after the flame
It is located after the flame in three different positions in order to investigate the influence of the porous medium’s location on the thermoacoustic instability.
Geometry

## Slide 27: Porous medium after the flame
β = 2 and d = 20 mm (most critical case investigated);
Porous zone parameters are the same of the previous case;
Thermal model: non-equilibrium additional source term in the energy conservation equation:
A solid zone is defined, and silicon carbide is the selected material to simulate the porous zone.
Setup of the simulation

## Slide 28: Porous medium after the flame
The porous medium is considered as a black box and, as a measure of the amount of energy transferred from the fluid to the solid matrix, it is taken into account the Number of Transfer Units NTU [3].
Setup of the simulation
[3] Abuserwal A.F., Pressure Drop and Forced Convective Heat Transfer in Porous Media,
Doctoral dissertation - University of Sheffield, 2012.

## Slide 29: Porous medium after the flame: results
Case | AE limit cycle amplitude [J]
Without porous medium | 2.1 · 10−1
Configuration 1 (250 mm from the flame) | 1.3 · 10−3
Configuration 2 (500 mm from the flame) | 4.8 · 10−4
Configuration 3 (750 mm from the flame) | 0
Configurations 1 and 2 reach a limit cycle state.
Instead, the last porous medium configuration decays, reaching a stable condition.
Although the first two setups develop a thermoacoustic instability, the limit cycle amplitude results are 2-3 orders of magnitude smaller than the reference case.

## Slide 30: Steps of the simulation
RANS
Constant heat source
URANS
Constant heat source
URANS
Unsteady heat addition
Acoustic fluctuations [4]
Mean flow
Mean flow
+
Unsteady, turbulent fluctuations
Mean flow
+
Turbulence fluctuations
+
Acoustic fluctuations
pa ̍̍̍
pt ̍̍̍
pt ̍̍̍
[4] S. Hubbard, A. P. Dowling. The triple decomposition of a fluctuating velocity field in a
multiscale flow. Physics of Fluids, 2015.

## Slide 31: Acoustic pressure : results
UNSTABLE CASE
CONFIGURATION 1
STABLE CASE
CONFIGURATION 3

## Slide 32: Acoustic temperature : results
UNSTABLE CASE
CONFIGURATION 1
STABLE CASE
CONFIGURATION 3

## Slide 33: Helmholtz resonator
Our annular Helmholtz resonator is composed of two main parts:
a cavity, of circular cross-section;
a neck that communicates with the outside through a small opening.

## Slide 34: Helmholtz resonator
Geometry
5 cases in total
385 Hz
3 cases: varying resonator’s geometry and fixing its position
2 cases: fixing resonator’s geometry and varying its position
[5]
[5] S. Hubbard, A. P. Dowling. Acoustic resonances of an industrial gas turbine combustion
system. ASME Journal of Engineering for Gas Turbines and Power, 123:766–773, 2001.

## Slide 35: Helmholtz resonator: results
Case | Geometry | Distance from the flame [mm] | Results
1 | I | 500 | stable
2 | II | 500 | stable
3 | III | 500 | stable
4 | II | 250 | unstable
5 | II | 750 | unstable
I
II
III

## Slide 36: Damping of the resonator
Acoustic pressure [Pa]
without resonator
Acoustic pressure [Pa]
with resonator
β=2, d=20 mm

## Slide 37: Damping of the resonator
Acoustic pressure [Pa]
without resonator
Acoustic pressure [Pa]
with resonator
β=2, d=20 mm

## Slide 38: Conclusions
Once dealt with two different approaches, linear and nonlinear, but the physics suggests to employ a nonlinear approach.
As concerns thermoacoustic damping:
  Porous media before the flame successfully damp thermoacoustic instabilities for many parametric conditions;
  A porous diaphragm after the flame is very effective, particularly when its position is carefully chosen;
  Helmholtz resonators are characterized by much smaller pressure losses than porous media and, provided a careful selection of their sizing and position is made, they prove to work very well.

## Slide 39: Thank you for your attention
Lorenzo Carrattieri
Giulia Innocenti