## Slide 1: Surrogate-Based Shape Optimisation for Aircraft Design: Implementation in CEASIOMpy
Author:
Marco Ilmi Rushani
Supervisors:
Prof. A. Bottaro
Ing. Jan B. Vos
Dr. Giacomo Benedetti
Notes: Prova prova

## Slide 2
Introduction & Motivation
Context
  Conceptual aircraft design requires rapid evaluation of many configurations
Challenge
  High-fidelity simulations are computationally expensive
Solution
  Enable fast and efficient design space exploration using surrogate models

## Slide 3: OUTLINE
Conceptual Aircraft Design Environment
CEASIOMpy Framework
Surrogate Modelling – Intuition
Surrogate Modeling Toolbox (SMT)
Validation Case: ONERA M6 Wing
Application: UAV Winglet Optimisation
Conclusions and future work

## Slide 4
Conceptual Aircraft Design Environment

## Slide 5: OUTLINE
Surrogate modeling: A Simple Example
Introduction & Motivation
Introduction & Motivation
CEASIOMpy Framework
Surrogate Modelling – Intuition
Surrogate Modeling Toolbox (SMT)
Validation Case: ONERA M6 Wing
Application: UAV Winglet Optimisation
Conclusions and future work

## Slide 6
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
_
DESIGN OF EXPERIMENTS
Problem: Optimizing Coffee Quality  Objective: Maximize Taste Score
DESIGN VARIABLES
        Coffee amount
        Water temperature
        Brewing time
| RANGE
  8 - 12 gr
  85 – 96 °
  20 – 35 s
Surrogate modeling: A Simple Example
Next step: DESIGN OF EXPERIMENTS

## Slide 7
3) EXPERIMENTS
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
_
DESIGN OF EXPERIMENTS
Problem: Optimizing Coffee Quality  Objective: Maximize Taste Score
Experiment | Coffee (g) | Temp (°C) | Time (s)
1 | 9.1 | 87.3 | 22.4
2 | 12.4 | 93.5 | 30.1
3 | 10.8 | 91.2 | 26.8
4 | 13.2 | 94.1 | 33.0
... | ... | ... | ...
30 | 11.3 | 92.0 | 27.5
 Sampling
Next step: EXPERIMENTS

## Slide 8
Coffee | Temp | Time | Aroma | Acidity | Aftertaste | Taste score
11.2 g | 92 °C | 27 s | 8.4 | 7.8 | 8.0 | 8.08
4) SURROGATE MODEL
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
EXPERIMENTS
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
Problem: Optimizing Coffee Quality  Objective: Maximize Taste Score
3) EXPERIMENTS
 Definition of taste score
Attribute | Score range
Aroma | 0–10
Acidity | 0–10
Aftertaste | 0–10
DATASET
Next step: Training the Surrogate Model

## Slide 9
TRAINING:
4) SURROGATE MODEL
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
EXPERIMENTS
Problem: Optimizing Coffee Quality  Objective: Maximize Taste Score
Chart: 
| TRAINING SET | VALIDATION SET | TEST SET
DATASET SPLITTING | 7 | 2 | 1
Used to adjust model hyperparameters.
Used to assess predictive accuracy.
Used to fit the surrogate model.

## Slide 10
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
EXPERIMENTS
SURROGATE MODEL
4) SURROGATE MODEL
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
EXPERIMENTS
Problem: Optimizing Coffee Quality  Objective: Maximize Taste Score
TRAINING:
VALIDATION:
TEST:
approximate the relationship between the design variables () and the objective function
tune the hyperparameters of the surrogate model
evaluate the predictive performance of the model
Where:
N  number of samples
 true value
 model prediction
The model learns from input–output data by adjusting its parameters to minimize prediction error.
REFINEMENT STRATEGY
Next step: Optimisation
5) OPTIMISATION

## Slide 11
From Concept to Application
DESIGN VARIABLES: Coffee amount, Water temperature, Brewing time
DESIGN OF EXPERIMENTS
EXPERIMENTS
SURROGATE MODEL
Problem: Optimizing Coffee Quality  Objective: Maximize Taste Score
5) OPTIMISATION

## Slide 12: OUTLINE
From Concept to Application
Introduction & Motivation
Introduction & Motivation
CEASIOMpy Framework
Surrogate Modelling – Intuition
Surrogate Modeling Toolbox (SMT)
Validation Case: ONERA M6 Wing
Application: UAV Winglet Optimisation
Conclusions and future work

## Slide 13
From Concept to Application
Surrogate Modeling Toolbox
An open-source Python library providing tools to build and implement surrogate models.

## Slide 14
Radial Basis Function (RBF) surrogate model :
Interpolation method that approximates unknown values from known data points;
Uses radial kernels centered on training samples to build a smooth surrogate model;
Notes: Interpolation method that approximates unknown values from known data points; Uses radial kernels centered on training samples to build a smooth surrogate model; Typically fast to train and evaluate;
🟢 No probabilistic assumptions required for the model
🟢 Works well with moderate to large datasets
🔴 Does not directly provide uncertainty estimates (unlike Kriging)

## Slide 15: OUTLINE
Validation case - ONERA M6
Validation case - ONERA M6
Introduction & Motivation
Introduction & Motivation
CEASIOMpy Framework
Surrogate Modelling – Intuition
Surrogate Modeling Toolbox (SMT)
Validation Case: ONERA M6 Wing
Application: UAV Winglet Optimisation
Conclusions and future work

## Slide 16
extensively used for CFD validation
available experimental and numerical reference data
DESIGN VARIABLES | VALUE
Sweep angle | 30°
Tip chord | 0.459 m
Semi-span | 0.595 m
Twist | 0°
Parameter | Value
Mach number | 0.84
Angle of attack | 0° – 5° (typical test range)
Validation case - ONERA M6
Notes: The ONERA M6 wing is a classical benchmark configuration used in aerodynamic studies. It is widely adopted to validate numerical methods and surrogate modeling approaches.

## Slide 17: Validation case - ONERA M6
SIMULATIONS
DESIGN VARIABLES | VALUE
Sweep angle | 30°
Tip chord | 0.459 m
Semi-span | 0.598 m
Twist | 0°
RANGE
27 – 33 [°]
0.436 – 0.482 [m]
0.575 - 0.620 [m]
(-1) ­– 1 [°]
LATIN HYPERCUBE SAMPLING (LHS)
 200 SAMPLES
Design Of Experiments

## Slide 18
SIMULATIONS
ATHENA VORTEX LATTICE
Vortex Lattice Method:
  Represents the lifting surfaces as a vortex surfaces,
  Neglects profile thickness and fluid viscosity.
Objective:
LIFT COEFFICIENT ()
ATHENA VORTEX LATTICE
Validation case - ONERA M6

## Slide 19: Validation case - ONERA M6
BEST CONFIGURATION
RBF SURROGATE MODEL
Split dataset and generate the model
AVL simulations results
OPTIMISATION: Powell Algorithm

## Slide 20
REFINEMENT STRATEGY
BEST CONFIGURATION
PARAMETER | BASELINE | OPTIMISED
SWEEP ANGLE [°] | 30 | 28.2
TIP CHORD [m] | 0.459 | 0.477
SEMI-SPAN [m] | 0.598 | 0.620
TWIST [°] | 0 | 0.93
[-] | 0.273 | 0.326
PARAMETER | BASELINE | OPTIMISED
SWEEP ANGLE [°] | 30 | 28.2
TIP CHORD [m] | 0.459 | 0.477
SEMI-SPAN [m] | 0.598 | 0.620
TWIST [°] | 0 | 0.93
 | 0.273 | 0.326
+19%
RMSE
0.021962
WHAT IF ?
Validation case - ONERA M6

## Slide 21
REFINEMENT STRATEGY
TRAIN SURROGATE MODEL
?
YES
NO
RESULTS
GENERATE AND EVALUATE NEW HIGH-FIDELITY POINTS
UPDATE TRAINING DATASET

## Slide 22
GENERATE AND EVALUATE NEW HIGH-FIDELITY POINTS
Leave-One-Out (LOO) Error
Design points
○ ● ● ● ●
● ○ ● ● ●
● ● ○ ● ●
● ● ● ○ ●
● ● ● ● ○
LOO evaluation
remove ○
train surrogate on remaining points
predict at that point
compute prediction error
Where:
: true value
: prediction of the surrogate model trained without sample i

## Slide 23
GENERATE AND EVALUATE NEW HIGH-FIDELITY POINTS
Adaptive Sampling
Select points with highest LOO error
High-fidelity evaluations
GMSH Module:
  Unstructured 3D Mesh with 1.5 millions of elements
SU2 Module: CFD Simulations with RANS’s Method
  Considering viscous effects
  Simulation time ~ 2 hours for 2000 iterations

## Slide 24
SET
GENERATE AND EVALUATE NEW HIGH-FIDELITY POINTS
Adaptive Sampling
Select points with highest LOO error
High-fidelity evaluations
Augment dataset
Retrain Surrogate Model
RMSE <
YES
NO
RESULTS

## Slide 25
42 NEW HIGH FIDELITY POINTS
Computational time: ~ 4 days
PARAMETER | LOW-FID | MULTI-FID
SWEEP ANGLE [°] | 28.2 | 27
TIP CHORD [m] | 0.477 | 0.477
SEMI-SPAN [m] | 0.62 | 0.62
TWIST [°] | 0.93 | 1.00
[-] | 0.326 | 0.363
PARAMETER | LOW-FID | MULTI-FID
SWEEP ANGLE [°] | 28.2 | 27
TIP CHORD [m] | 0.477 | 0.477
SEMI-SPAN [m] | 0.62 | 0.62
TWIST [°] | 0.93 | 1.00
 | 0.326 | 0.363
AVL VALIDATION: 0.352
RANS VALIDATION: 0.368

## Slide 26: OUTLINE
Winglet optimisation for the UAV configuration
Introduction & Motivation
Introduction & Motivation
CEASIOMpy Framework
Surrogate Modelling – Intuition
Surrogate Modeling Toolbox (SMT)
Validation Case: ONERA M6 Wing
Application: UAV Winglet Optimisation
Conclusions and future work

## Slide 27
Design variables:
• Dihedral ↑ towards tip
• Chord ↓ towards tip
• Twist → local variation allowed
• Sweep → non-uniform bounds
Objective: max()
Winglet optimisation for the UAV configuration

## Slide 28
SAMPLES | RMSE
5000 | 0.027561
SAMPLES | RMSE
1000 | 0.038291
3000 | 0.031280
5000 | 0.027561
RBF MODEL
70/20/10 split
Progressively larger set of samples
SAMPLES | RMSE
1000 | 0.038291
3000 | 0.031280
5000 | 0.027561
Winglet optimisation for the UAV configuration

## Slide 29
 | BASELINE | OPTIMISED
 | 1.21 | 1.36
 | BASELINE | OPTIMISED
 | 1.21 | 1.36
↓ DIHEDRAL ANGLE
↓ SWEEP ANGLE
↑ CHORD
↑ TWIST
✅ AVL VALIDATION 
✅ STATIC STABILITY
Winglet optimisation for the UAV configuration
SAMPLES | RMSE
5000 | 0.027561

## Slide 30
… other sections
PREDICTED VALUE:
✅ AVL VALIDATION 
✅ STATIC STABILITY
+6%
BASELINE
Winglet optimisation for the UAV configuration

## Slide 31: OUTLINE
Conclusions and Perspectives
Introduction & Motivation
Introduction & Motivation
CEASIOMpy Framework
Surrogate Modelling – Intuition
Surrogate Modeling Toolbox (SMT)
Validation Case: ONERA M6 Wing
Application: UAV Winglet Optimisation
Conclusions and future work

## Slide 32
Key Contributions
Development of a surrogate-based optimisation workflow in CEASIOMpy
Integration of:
  Direct control and variation of geometric design parameters defined in CPACS
  Machine learning surrogate models (RBF)
  Adaptive multi-fidelity refinement (AVL + SU2)
Demonstration of:
  Accurate trend prediction (low-fidelity)
  Improved quantitative accuracy (multi-fidelity)
Conclusions and Perspectives

## Slide 33
Future work
Integration of constraint-aware optimisation
  inclusion of geometric and regulatory constraints within the loop
Extension to multi-objective optimisation
  lift, drag, stability, mission requirements
Development of multidisciplinary optimisation (MDO)
  coupling with structures, propulsion, mission analysis
Conclusions and Perspectives

## Slide 34: Thank you for your attention
Questions?