## Slide 1: FOILING MOTH CENTERBOAD ON OpenFOAM
COURSE: ADVANCED FLUID DYNAMICS
PROFESSOR: JAN PRALITS
STUDENT: ALESSANDRO CHIAPPALONE

## Slide 2: INTRODUCTION
WHAT IS A MOTH ?
FEATURES:
LIGHT
FAST
FUNNY
HOW CAN IT FLY?

## Slide 3: SETTING THE PROBLEM
TARGETS:
Study of fluid dynamics around the centerboard with a flow of 5m/s
Determination of Cl and Cd for the centerboard in 5 different geometries
Determination of the minimun Cl for a total weight of 100 kg
FUNDAMENTALS PARAMETERS:
Variable | Mean | Unit | Value
c | Water Velocity | [m/s] | 5
L | Characteristic Length | [m] | 0,11
υ | Kinematic Viscosity | [m2/s] | 1.2 10-6
Re | / | / | 458332

## Slide 4: NUMERICAL SOLVER
EQUATION TO SOLVE:
SOLVER CHOSED: SimpleFoam
Based on RANS analysis

## Slide 5: BOUNDARY CONDITIONS
The fluid domain is represented by a parallelepiped with an X side of 12 [m] an Y side of 2.4 [m] and a Z side of 2.5 [m]. X is the streamwise direction, Z axe is the lift direction (vertical).
VELOCITY
PRESSURE

## Slide 6: GEOMETRY
CREATED BY USING THE INVENTOR CAD SOFTWARE
BASED ON GARDA TOP 3 GEOMETRY
 | Section | Span [mm] | Chord[mm]
Centreboard | NACA 0012 | 1000 | 120
Centreboard Foil | NACA 63412 | 860 | 110

## Slide 7: GEOMETRY
TO STUDY THE Cl VARIATION HAS BEEN USED 5 DIFFERENT GEOMETRIES
Trailing edge flap’s angle | CAD Model
-10° | 
-5° | 
0° | 
5° | 
10° | 

## Slide 8: MESHING
:Mesh has been done in 4 steps:
BlockMesh command to make a mesh of the control volume
[54 8 8]
Research of the best compromise between refinement surfaces edges and the calculator’s power.

## Slide 9: MESHING
USE The addLayer tool to refine the mesh close the surfaces
Increase the refinement beside the centerboard where there is turbulence.

## Slide 10: RESULTS
Numerical simulations always need a grid convergence study.
This study was done only on the geometry with 0° for trailing edge flaps but it’s applicable also on the other geometries.
Cell’s number | CL | CD
136000 | 1,0802 | 0,384936
643000 | 0,84637 | 0,248135
1550000 | 0,849123 | 0,269452
2550000 | 0,860901 | 0,279953
3740000 | 0,859068 | 0,276287

## Slide 11: RESULTS
Some parameter are important for a good simulation
The yPlus: is a non dimensional quantity calculated close to wall. To have a good simulation this value must to be between 10 and 300.
Residuals and time-step continuity: Residuals have to be much lower as possible to obtain a good simulation. Generally the residuals should be lower than 10-4 – 10-5. To respect the mass conservation law it is essential that this value is lower as possible. Usually a number lower than 10 -11 – 10-12 is acceptable.
How is possible to obatain this value?
It is necessary to work on the mesh and in particular on the layers near the walls. (RefineWallLayer)
Trailing edge flap’s angle | Centerboard’s yPlus max | Ship’s yPlus max
-10 | 295 | 186
-5 | 280 | 150
0 | 175 | 165
5 | 255 | 145
10 | 260 | 165

## Slide 12: RESULTS
Pressure and Velocity:
Flap’s angle | Pressure Distribution | Velocity Distribution
-10° |  | 
-5° |  | 
0° |  | 

## Slide 13
5° |  | 
10° |  | 
And for the symmetric profile?

## Slide 14: RESULTS
WATH ABOUT THE Cl-Cd VALUES AND TRENDS ?

## Slide 15: RESULTS
To find the minimum value needed of CL for 5 m/s we supposed a total weight of 100 kg (boat + skipper).
The solution give:
CL= 0.834
Variable | Mean | Unit | Value
c | Water Velocity | [m/s] | 5
A | Approximated foil area | [m2] | 0,094
ρ | Water Density | [Kg/m3] | 1000
mg | Boat Weight Force | [N] | 981
where

## Slide 16: CONCLUSION
We obtained that :
Lift is generated with a NACA 63412 in each case except the case with -10° flap’s angle.
The angle with lower drag and a positive lift is -5°
To lift a total weight of 100 kg ( boat + skipper) it is necessary work with a flap angle higher than 0° with a speed of 5 m/s
FUTURE DEVELOPMENTS
The flap’s angle is determined by the speed of the ship trough the sensor called wand (reported in figure 1.1. )
The hull surging over the sea level causes a big drag fall which is not considered in this study.
Improve the speed variation to study lift and drag in function of the hull’s velocity.

## Slide 17
THANKS FOR THE ATTENTION