## Slide 1: Implementation of a two stage drying model for liquid drops containing insoluble solids in OpenFOAM for spray drying application
University of Genoa, Polytechinc School DIME
Department of Mechanical, Energy, Management and Transportation Engineering
Candidate: Giovanni Beati
Supervisor: Prof. Ing. Jan Oscar Pralits (Unige)
Co Supervisor: Dott. Ing. Matteo Colli (Unige)
Marco Atzori (KTH)
July 2017

## Slide 2
What is Spray Drying
Spray Drying is a widely use industrial process that involves the transformation of a liquid feed containing solid fraction into particles by supplying the feed as a spray into a chamber with a hot drying agent.

## Slide 3
What is Spray Drying
CFD
Spray Drying is a widely use industrial process that involves the transformation of a liquid feed containing solid fraction into particles by supplying the feed as a spray into a chamber with a hot drying agent.
Droplets coloured with temperature ( =19 °C , =197 °C)

## Slide 4: Thesis purpose and outline
This work is part of a project started last year by Stefano Pastorino in collaboration with the DICCA department. In his master thesis, he first began to treat spray drying modelling in OpenFOAM.

## Slide 5: Thesis purpose and outline
Purpose Study and implementation of the two stage drying model in a CFD code (OpenFOAM)
This work is part of a project started last year by Stefano Pastorino in collaboration with the DICCA department. In his master thesis, he first began to treat spray drying modelling in OpenFOAM.

## Slide 6: Thesis purpose and outline
STEP 1: Python implementation of the two-stage model for a motionless droplet + comparison with experimental data.
Purpose Study and implementation of the two stage drying model in a CFD code (OpenFOAM)
This work is part of a project started last year by Stefano Pastorino in collaboration with the DICCA department. In his master thesis, he first began to treat spray drying modelling in OpenFOAM.

## Slide 7: Thesis purpose and outline
STEP 1: Python implementation of the two-stage model for a motionless droplet + comparison with experimental data.
Purpose Study and implementation of the two stage drying model in a CFD code (OpenFOAM)
This work is part of a project started last year by Stefano Pastorino in collaboration with the DICCA department. In his master thesis, he first began to treat spray drying modelling in OpenFOAM.
STEP 2: OpenFOAM implementation: the two-stage drying model is applied along the droplets trajectories.

## Slide 8: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
1-ST Drying stage: Evaporation occurs on the surface resulting in droplet diameter shrinking until is reached.
*Mezhericher, Levy, Borde 2007

## Slide 9: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
1-ST Drying stage: Evaporation occurs on the surface resulting in droplet diameter shrinking until is reached.
*Mezhericher, Levy, Borde 2007

## Slide 10: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
1-ST Drying stage: Evaporation occurs on the surface resulting in droplet diameter shrinking until is reached.
*Mezhericher, Levy, Borde 2007

## Slide 11: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
2-ST Drying stage: When is reached a solid crust surrounds a wet core: water vapour diffuses through the crust pores.
*Mezhericher, Levy, Borde 2007

## Slide 12: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
2-ST Drying stage: When is reached a solid crust surrounds a wet core: water vapour diffuses through the crust pores.
*Mezhericher, Levy, Borde 2007

## Slide 13: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
2-ST Drying stage: When is reached a solid crust surrounds a wet core: water vapour diffuses through the crust pores.
*Mezhericher, Levy, Borde 2007

## Slide 14: Two Stage Evaporation Model
The drying kinetic of liquid drops containing solid can be separated in two main stages.
2-ST Drying stage: When is reached a solid crust surrounds a wet core: water vapour diffuses through the crust pores.
*Mezhericher, Levy, Borde 2007

## Slide 15: The first drying stage
Initial values*:
Motionless Droplet:
Water drop + Silica nanoparticles
D= 2 mm
T= 19 °C
c=30% (initial solid content)
=2.3 (moisture content)
m=4.3 mg
*Nesic and Vodnik, 1989
Drying air:
Relative Humidity=0.4%
T=178 °C
|U|=1.4 m/s
= (First drying stage occurs until )
is the critical moisture content derived from a certain average solid to liquid ratio.

## Slide 16: The first drying stage
Droplet equation:
Convective heat transfer (h):
Mass transfer equations:
Convective mass transfer ():

## Slide 17: The first drying stage
Droplet equation:
Convective heat transfer (h):
Mass transfer equations:
Convective mass transfer ():

## Slide 18: The first drying stage
Droplet equation:
Convective heat transfer (h):
Mass transfer equations:
Convective mass transfer ():

## Slide 19: The first drying stage
Droplet equation:
Convective heat transfer (h):
Mass transfer equations:
Convective mass transfer ():

## Slide 20: The first drying stage
Moving boundary problem: it requires an implicit itherative algorithm
Landau’s transformation:
Transformed equation:
Transformed BC:

## Slide 21: The first drying stage
*Comparison with Nesic and Vodnik, 1989

## Slide 22: The second drying stage
Wet core equation:
Crust equation :

## Slide 23: The second drying stage
Wet core equation:
Crust equation :

## Slide 24: The second drying stage
Mass transfer equation: the evaporation rate is expressed as:
Moving crust-wet core interface:
Landau’s tranformation and implicit itherative algorithm are required to solve both wet core and crust energy equations

## Slide 25: The second drying stage
Differences from experimental data due to difficulties to model the vapour diffusion through the crust pores.
*Comparison with Nesic and Vodnik, 1989

## Slide 26: CFD: Spray Drying Modelling
Original Geometry
Simplifications in the geometry have been adopted to have a cheaper study case
The purpose is now to implement the two stage drying model in OpenFOAM (Open Source CFD code)
Modified Geometry
Notes: Avevo a disposizione la geomtria originale ……

## Slide 27: CFD: Spray Drying Modelling
Original Geometry
Simplifications in the geometry have been adopted to have a cheaper study case
The purpose is now to implement the two stage drying model in OpenFOAM (Open Source CFD code)
Modified Geometry
Notes: Avevo a disposizione la geomtria originale ……

## Slide 28: CFD: Spray Drying Modelling
Particles have been injected when a steady state condition for the base flow has been obtained.
Numerical model:
Mesh 460k cells
buoyantPimpleFoam solver
k-ω SST
Steady state reached at 170 s
Notes: Le particelle saranno iniettate in alto al centro soltanto quando….

## Slide 29: CFD: Mutiphase flow with particles
Multiphase flow:
Air: continuous phase (Eulerian approach)
Particles: dispersed phase (Lagrangian approach)
Particles hypotesis:
Sphere
Diluite regime
One-way coupling: continuous phase  dispersed phase

## Slide 30: CFD: Mutiphase flow with particles
How does the CFD code perform the Lagrangian particle tracking ?
For each droplet the equation of dynamic is solved:
Assumption:
Only the drag force evaluated through a drag coefficient is considered:

## Slide 31: Implementation of the new Lagrangian solver
Implementation of a new OpenFOAM application
Add to the already existing buoyantPimpleFoam solver (for the solution of the Eulerian field) the Lagrangian tracking of particles with the two stage evaporation model included.
This resulted in the buoyantKinematicParcelFoam solver.

## Slide 32: Implementation of the new Lagrangian solver
Definition of the Lagrangian time-step δt< Δt

## Slide 33: Implementation of the new Lagrangian solver
Evaluation of the new position:
Definition of the Lagrangian time-step δt< Δt

## Slide 34: Implementation of the new Lagrangian solver
Definition of the Lagrangian time-step δt< Δt
Evaluation of the new position:
Two stage drying model
Assignement of new: R, T, X (moisture content)

## Slide 35: Implementation of the new Lagrangian solver
Definition of the Lagrangian time-step δt< Δt
Evaluation of the new position:
Two stage drying model
Assignement of new: R, T, X (moisture content)
Update the cell based properties for the new position and evaluation of the new particle velocity

## Slide 36: Implementation of the new Lagrangian solver
First drying stage simplifications:
With micron sized droplets the temperature profile is neglected*
The droplet equation of energy conservation becomes:
Smaller computational costs
*According to Mezhericher et al., 2012

## Slide 37: Implementation of the new Lagrangian solver
First drying stage simplifications:
With micron sized droplets the temperature profile is neglected*
The droplet equation of energy conservation becomes:
Smaller computational costs
Second drying stage simplifications:
The droplet is considered to be completely dried without further evaporation.
The particle equation of energy conservation is now:
*According to Mezhericher et al., 2012

## Slide 38
buoyantKinematicParcelFoam c=0,3%
reactingParcelFoam

## Slide 39
buoyantKinematicParcelFoam c=0.3%
reactingParcelFoam

## Slide 40
reactingParcelFoam
buoyantKinematicParcelFoam c=0.3%

## Slide 41
buoyantKinematicParcelFoam c=30%

## Slide 42
buoyantKinematicParcelFoam c=30%

## Slide 43
buoyantKinematicParcelFoam c=30%

## Slide 44: Conclusions
The two stage drying model has been studied and implemented in a simplified environment showing good agreement with experimental data especially for the first drying stage.
Then the model has been integrated in OpenFOAM resulting in the new application buoyantKinematicParcelFoam.

## Slide 45: Future developments
The OpenFOAM implementation should be improved in order to:
make the application more user friendly through the use of dictionaries for the droplets features.
Implementation in OpenFOAM of a more detailed second drying stage.
Tests using the geometry already presented by Stefano Pastorino.